## Slide 1: Unit 2 – Network Communication Concepts

## Slide 2: Contents
Parallel & Serial Communication
Synchronous & Asynchronous Communication
Modes of Communication: Simplex, Half-Duplex, Full-Duplex
Multiplexing, De-Multiplexing: FDM, TDM
Communication Media: Guided Media, Unguided Media
Switching Techniques: Circuit Switching, Message Switching, Packet Switching

## Slide 3: Parallel & Serial Communication

## Slide 4: Parallel & Serial Communication

## Slide 5: Parallel & Serial Communication

## Slide 6: Contents
Parallel & Serial Communication
Synchronous & Asynchronous Communication
Modes of Communication: Simple, Half-Duplex, Full-Duplex
Multiplexing, De-Multiplexing: FDA, TDM
Communication Media: Guided Media, Unguided Media
Switching Techniques: Circuit Switching, Message Switching, Packet Switching

## Slide 7: Synchronous & Asynchronous Communication
In synchronous transmission, we send bits one after another without start or stop bits or gaps. It is the responsibility of the receiver to group the bits.

## Slide 8: Synchronous & Asynchronous Communication
In asynchronous transmission, we send 1 start bit (0) at the beginning and 1 or more stop bits (1s) at the end of each byte. There may be a gap between each byte.

## Slide 9: Synchronous & Asynchronous Communication
Asynchronous here means “asynchronous at the byte level, but the bits are still synchronized; their duration is the same.

## Slide 10: Contents
Parallel & Serial Communication
Synchronous & Asynchronous Communication
Modes of Communication: Simplex, Half-Duplex, Full-Duplex
Multiplexing, De-Multiplexing: FDM, TDM
Communication Media: Guided Media, Unguided Media
Switching Techniques: Circuit Switching, Message Switching, Packet Switching

## Slide 11: Modes of Communication: Simplex, Half-Duplex, Full-Duplex
Communication between two devices can be:
  Simplex
  Half-Duplex
  Full-Duplex

## Slide 12: Modes of Communication: Simplex
One way street
The communication is unidirectional
Only one device on a link can transmit; the other can only receive
Use the entire capacity of the channel to send data
Example: Keyboards, Monitors

## Slide 13: Modes of Communication: Half-duplex
One-lane with two-directional traffic.
Each station can both transmit and receive, but not at the same time
When one device is sending, the other can only receive, and vice versa
The entire capacity of a channel is taken over by the transmitting device
Example: Walkie-talkies
Data
Data

## Slide 14: Modes of Communication: full-duplex
Two way street
Both stations can transmit and receive at same time
Signals going in either direction sharing the capacity of the link
Sharing can occur in two ways:
  Link has two physically separate transmission paths
    One for sending and the other for receiving
  The capacity of the channel is divided between signals travelling in both directions
Example: Telephone network
Data
Data

## Slide 15: Contents
Parallel & Serial Communication
Synchronous & Asynchronous Communication
Modes of Communication: Simplex, Half-Duplex, Full-Duplex
Multiplexing, De-Multiplexing: FDM, TDM
Communication Media: Guided Media, Unguided Media
Switching Techniques: Circuit Switching, Message Switching, Packet Switching

## Slide 16: Multiplexing, De-Multiplexing: FDM, TDM
The communication takes place by transmission of data from one place to the other.
This requires transforming data from one type to another.
Typically to send data from place A to place B, the digital data is converted into signals which are then transferred through telephone lines, optical fiber cables or wireless mediums.
Normally, there is a single channel that carries multiple signals from place A to place B.
Like, single wire from electricity pole carrying electricity for whole apartment, instead of having one wire for each apartment from the pole.
This is called multiplexing.

## Slide 17: Multiplexing, De-Multiplexing: FDM, TDM
On receiving end, the signals are separated from channel.
This process is called de-multiplexing.

## Slide 18: Multiplexing, De-Multiplexing: FDM, TDM
Bandwidth utilization is the wise use of available bandwidth to achieve specific goals.
Efficiency can be achieved by multiplexing; i.e., sharing of the bandwidth between multiple users.
Whenever the bandwidth of a medium linking two devices is greater than the bandwidth needs of the devices, the link can be shared.
Multiplexing is the set of techniques that allows the (simultaneous) transmission of multiple signals across a single data link.
As data and telecommunications use increases, so does traffic.

## Slide 19: Multiplexing, De-Multiplexing: FDM, TDM

## Slide 20: Multiplexing, De-Multiplexing: FDM, TDM
Categories of multiplexing:

## Slide 21: Multiplexing, De-Multiplexing: FDM, TDM
Frequency-division multiplexing (FDM)
  FDM is an analog multiplexing technique that combines analog signals.
  It uses the concept of modulation discussed in Ch 5.

## Slide 22: Multiplexing, De-Multiplexing: FDM, TDM
FDM Process

## Slide 23: Multiplexing, De-Multiplexing: FDM, TDM
FDM

## Slide 24: Multiplexing, De-Multiplexing: FDM, TDM
FDM De-Multiplexing example

## Slide 25: Multiplexing, De-Multiplexing: FDM, TDM
Time Division Multiplexing (TDM)

## Slide 26: Multiplexing, De-Multiplexing: FDM, TDM
TDM is a digital multiplexing technique for combining several low-rate digital channels into one high-rate one.

## Slide 27: Multiplexing, De-Multiplexing: FDM, TDM
Synchronous time-division multiplexing
  In synchronous TDM, the data rate of the link is n times faster, and the unit duration is n times shorter.

## Slide 28: Multiplexing, De-Multiplexing: FDM, TDM

## Slide 29: Contents
Parallel & Serial Communication
Synchronous & Asynchronous Communication
Modes of Communication: Simplex, Half-Duplex, Full-Duplex
Multiplexing, De-Multiplexing: FDM, TDM
Communication Media: Guided Media, Unguided Media
Switching Techniques: Circuit Switching, Message Switching, Packet Switching

## Slide 30: Communication Media: Guided Media, Unguided Media

## Slide 31: Communication Media: Guided Media, Unguided Media
Guided media, which are those that provide a conduit from one device to another, include twisted-pair cable, coaxial cable, and fiber-optic cable.

## Slide 32: Communication Media: Guided Media, Unguided Media
Twisted Pair Cable

## Slide 33: Communication Media: Guided Media, Unguided Media
UTP and STP cables

## Slide 34: Communication Media: Guided Media, Unguided Media
Categories of unshielded twisted-pair cables

## Slide 35: Communication Media: Guided Media, Unguided Media
UTP connector

## Slide 36: Communication Media: Guided Media, Unguided Media
Coaxial cable

## Slide 37: Communication Media: Guided Media, Unguided Media
BNC connectors

## Slide 38: Communication Media: Guided Media, Unguided Media
Optical fiber

## Slide 39: Communication Media: Guided Media, Unguided Media
Optical Fiber
  Propagation modes

## Slide 40: Communication Media: Guided Media, Unguided Media
Optical Fiber – Modes

## Slide 41: Communication Media: Guided Media, Unguided Media
Fiber construction

## Slide 42: Communication Media: Guided Media, Unguided Media
Fiber-optic cable connectors

## Slide 43: Communication Media: Guided Media, Unguided Media
Unguided media transport electromagnetic waves without using a physical conductor. This type of communication is often referred to as wireless communication

## Slide 44: Communication Media: Guided Media, Unguided Media
Electromagnetic spectrum for wireless communication

## Slide 45: Communication Media: Guided Media, Unguided Media
Propagation methods

## Slide 46: Communication Media: Guided Media, Unguided Media
Wireless transmission waves

## Slide 47: Communication Media: Guided Media, Unguided Media
Radio waves are used for multicast communications, such as radio and television, and paging systems. They can penetrate through walls.
Highly regulated. Use omni directional antennas

## Slide 48: Communication Media: Guided Media, Unguided Media
Microwaves are used for unicast communication such as cellular telephones, satellite networks,and wireless LANs.
Higher frequency ranges cannot penetrate walls.
Use directional antennas - point to point line of sight communications.

## Slide 49: Communication Media: Guided Media, Unguided Media
Infrared signals can be used for short-range communication in a closed area using line-of-sight propagation.

## Slide 50: Communication Media: Guided Media, Unguided Media
Wireless communication channels
  Are subject to a lot more errors than guided media channels.
  Interference is one cause for errors, can be circumvented with high SNR.
  The higher the SNR the less capacity is available for transmission due to the broadcast nature of the channel.
  Channel also subject to fading and no coverage holes.

## Slide 51: Contents
Parallel & Serial Communication
Synchronous & Asynchronous Communication
Modes of Communication: Simplex, Half-Duplex, Full-Duplex
Multiplexing, De-Multiplexing: FDM, TDM
Communication Media: Guided Media, Unguided Media
Switching Techniques: Circuit Switching, Message Switching, Packet Switching

## Slide 52: Switching Techniques: Circuit Switching, Message Switching, Packet Switching

## Slide 53: Switching Techniques: Circuit Switching, Message Switching, Packet Switching

## Slide 54: Switching Techniques: Circuit Switching, Message Switching, Packet Switching
Circuit Switching
  A circuit-switched network consists of a set of switches connected by physical links.
  A connection between two stations is a dedicated path made of one or more links.
  However, each connection uses only one dedicated channel on each link.
  Each link is normally divided into n channels by using FDM or TDM.

## Slide 55: Switching Techniques: Circuit Switching, Message Switching, Packet Switching

## Slide 56: Switching Techniques: Circuit Switching, Message Switching, Packet Switching
In circuit switching, the resources need to be reserved during the setup phase; the resources remain dedicated for the entire duration of data transfer until the teardown phase.

## Slide 57: Switching Techniques: Circuit Switching, Message Switching, Packet Switching
Switching at the physical layer in the traditional telephone network uses the circuit-switching approach.

## Slide 58: Switching Techniques: Circuit Switching, Message Switching, Packet Switching
The complete physical connection is established before any data can be exchanged.
Since circuits are switched it gets it’s name.
Earlier switching was done manually. There was an operator who would reside in switching office and plug a jumper connecting input & output sockets. Now switching is done automatically.

## Slide 59: Switching Techniques: Circuit Switching, Message Switching, Packet Switching
Packet Switching
  In data communications, we need to send messages from one end system to another.
  If the message is going to pass through a packet-switched network, it needs to be divided into packets of fixed or variable size.
  The size of the packet is determined by the network and the governing protocol.
The packets are handled in two ways
  Datagram
  Virtual Circuit

## Slide 60: Switching Techniques: Circuit Switching, Message Switching, Packet Switching
No physical copper path is established in advance between the sender and the receiver as in circuit switching.
Instead, the sent data is first stored in the first switching office and then forwarded later, one hop at a time.
Each block is received entirely, inspected for errors, and then retransmitted. This procedure continues until message reaches its destination. Owing to its working principle, it is also known as store and forward.

## Slide 61: Switching Techniques: Circuit Switching, Message Switching, Packet Switching
Datagram
  Each packet treated independently
  Packets can take any practical route
  Packets may arrive out of order
  Packets may get lost or delayed
  Up to receiver to re-order packets and recover from missing packets
Virtual Circuit
  Preplanned route established before any packets sent
  Call request and call accept packets establish connection (handshake)
  Each packet contains a virtual circuit identifier instead of destination address
  No routing decisions required for each packet
  Clear request to drop circuit
  Not a dedicated

## Slide 62: Switching Techniques: Circuit Switching, Message Switching, Packet Switching
Virtual Circuit vs. Datagram Switching

## Slide 63: Switching Techniques: Circuit Switching, Message Switching, Packet Switching
A datagram network with four switches (routers)

## Slide 64: Switching Techniques: Circuit Switching, Message Switching, Packet Switching
In virtual-circuit switching, all packets belonging to the same source and destination travel the same path; but the packets may arrive at the destination with different delays if resource allocation is on demand.

## Slide 65: Switching Techniques: Circuit Switching, Message Switching, Packet Switching